## Slide 1
AGRICULTURAL DRONES • PRECISION SPRAYING
Electrostatic Spray Charging for Drones
Cutting spray drift by 75% — a drone-ready retrofit.
75%
drift reduction
3×
leaf deposition
50%
chemical saving
Confidential proposal • September 2025
ONE NUMBER
$18,000
wasted per 1,000 ha / season on drifted chemical
Conventional: 35% on target
Electrostatic: 78% on target
U. of Georgia field trials

## Slide 2
The problem: most spray misses the leaf
Wind 10–15 km/h • altitude 2–3 m • conventional hydraulic nozzle
2
✛ SPRAY DRONE
spray
wind 10–15 km/h
drift cloud: 15–30 m
crop row — only ~35% lands here
40% lost
of every tank drifts away
< 5% reach
the leaf underside where pests live

## Slide 3
What drift costs — per hectare
$0.22/L chemical • 150 L/ha • 40% drift (conventional)
3
SPEND
$33.00
chemical per hectare per pass
DRIFTS AWAY
$13.20
60 litres lost to wind
WORKS
$19.80
only this part hits the leaf
Electrostatic keeps $9.24/ha on the leaf → $9,240 per 1,000 ha per season → hardware pays back in < 25 ha.

## Slide 4
Nobody selling spray drones charges the droplets
DJI • XAG • Hylio • Deere • ESS — all hydraulic or ground-only
4
DJI Agras
$15–25K
✕
no charging
XAG P100
$12–20K
✕
no charging
John Deere
$150K+
✕
ground only
ESS rigs
$5–15K
✕
ground only
5 barriers kept charging off drones — HV weight • arcing near LiPo • charge saturation • awareness • legal grey zone. Our design clears all five (next slides).

## Slide 5
Solution: charge each droplet as it leaves the nozzle
Induction charging • 6–12 kV • 10–50 µA • fits existing nozzles
5
1 PUMP
0.2–0.5 MPa 100–300 µm
2 CHARGE
induction ring 6–12 kV
3 FLY
0.5–2.0 mC/kg repel = no clump
4 STICK
wraps leaf + underside
WHY IT WORKS
leaf
Leaf is grounded through soil → field lines pull droplets around and under. 40–60% reach the underside (vs ~5% before).

## Slide 6
System architecture — 4 layers
CAN bus links every layer • STM32G4 at the centre
6
LAYER 1 — FLIGHT
ArduPilot + RTK → spray commands over CAN / MAVLink
LAYER 2 — CONTROL
STM32G4 → PID voltage per nozzle + current limit + prop-kill interlock
LAYER 3 — SPRAY ×4
HV PSU (12 V → 16 kV) → induction ring → hydraulic nozzle
LAYER 4 — POWER
12 V rail → isolated HV → ADC feedback (1000:1) + 50 µA cap
C A N b u s

## Slide 7
Control loop — per nozzle, every 5 ms
PID on voltage • hard current cap • fail-safe by default
7
Target voltage via CAN
Measure HV (ADC)
V = target?
no
Adjust DAC (PID)
yes
Current < 50 µA?
yes
✔ HOLD + SPRAY
no
✕ FAULT → kill props
SAFETY RULES
• 50 µA hard cap
• 16 kV ceiling
• HV fault = instant prop-kill
• Default state = OFF
Wind-adaptive mode: IMU estimates crosswind → voltage auto-tunes 6–12 kV.

## Slide 8
Research proof — 4 papers, one verdict
Full DOIs in closing slide • verified via Semantic Scholar
8
Zhang 2017
59 cit.
First UAV system · 2–3× deposition
Hanif 2022
82 cit.
“Most promising” + CAN control
★ TOP VERDICT
Li 2025
11 cit.
Two-stage · 1.62 mC/kg
Zhao 2024
17 cit.
Orchard-proven contact charging
+ Zhang & Huang 2021 (27 cit.): China has 200,000+ spray drones, <5% electrostatic • Hu & Kaizu 2022 (28 cit.): 30–50% waste cut

## Slide 9
Field proof — University of Georgia
Cotton / peanut / soybean • 5–15 km/h wind
9
ON-TARGET DEPOSITION
Conventional 35%
Electrostatic 78%
LEAF-UNDERSIDE REACH
Conventional ~5%
Electrostatic 50%
75%
drift cut
$10/ac
saved
8 kV
field sweet-spot
Orchards: 10–12 kV

## Slide 10
Roadmap → patent → product
File provisional BEFORE any publication
10
P1 · 4–6 w
Bench rig 1 nozzle
P2 · 6–8 w
4-nozzle CAN system
P3 · 4–6 w
Flight trials field data
P4
Patent → license
ASK: approve the single-nozzle bench rig → field data → provisional patent. Hardware ≈ $185/drone · payback < 25 ha.
Refs: Zhang 2017 DOI:10.25165/IJABE.V10I6.3460 • Li 2025 DOI:10.3390/agronomy15071641 • Hanif 2022 (82 cit.) • Hu & Kaizu 2022 (28 cit.) • Thank you.